## Slide 1: Project 4: Flow Control
Daniel Krizak and Alex Sweet
12/06/17

## Slide 2: Reactor Scheme

## Slide 3: Variable Declarations
F1- mass flowrate of stream 1 (kg/s)
t- time- (s)
Fout – outlet flow rate (kg/s)

## Slide 4: Constants/ Parameters
T1: 25°C ; T2:75 °C ; Tt(0): 50
F2: 5kg/s
Mt(0): 100kg
F1(0)= 5kg/s
F1(10)= 4 kg/s
dF1/dt: -.1 kg/s

## Slide 5: Mass Balance
In - out + generation + CV = CV + accumulation
F1 + F2 - Fout + rV = dM/dt
Accumulation and generation are 0, so
Fout = (F1 + F2)
The control volume has constant mass such that the sum of inlet flow and the outlet flow are equal

## Slide 6: Mass Flows

## Slide 7: Energy Balance
In - out + generation = accumulation
There is no generation or accumulation therefore the outlet is equal to the inlet flows
F1*T1+F2*T2 = (F1+F2)*Tout

## Slide 8: Energy Balance
F1*T1 + F2*T2 = (F1+F2)*Tout
F1 is the only non constant in the energy balance
F1 = F1in - (dF1/dt) from 1 to 10 seconds.

## Slide 9: Adding the Control Volume
While the Control volume has no impact on the mass flow amounts of input or output, the thermal balance is impacted because it creates a non-instantaneous response in the outlet temperature.

## Slide 10: New outlet (accounting for CV)
F1*T1 + F2*T2 + 100*T(0) = (F1+F2+100)*Tout
Where F1= 5 -0.1t for 0<t<10
and F1= 4 at 10<t
Flow energy balance
New terms to account for CV

## Slide 11: Steady State Approach
No accumulation or generation:
In = out at t -> Ꝏ
25 ° *4+75 ° *5= 9*Tout
Tout = 52.77777777777°F
We should find this Tout value if we allow the program running for a sufficient number of runs

## Slide 12: Integral Solution
The integral method breaks the time down into equal segments of step size which are summed over the integral of each area to converge on the final solution.

## Slide 13: 4th Order (Runge) Method

## Slide 14: Program Variables and Parameters
M= initial mass (CV)
T1= temp in stream 1
T2= temp in stream 2
F1= flow of stream 1
t= time; t0= initial; tf= final

## Slide 15: More Program Variables
IntX: array for x values solved by integration
IntY: array for y values solved by integration
RkX: array for x values solved by range
RkY: array for y values solved by range
Steps= numstep= (50) number of times the interval has been divided equally (used in sizing arrays)

## Slide 16: More Program Variables
Time interval given by t(0) and tf values
Step size gives the step length value

## Slide 17: Coded Energy Balance
Solved for temperature of the tank which for a cstr is modeled as equal to the temperature at the outlet

## Slide 18: Bonus Section
The bonus section requires the addition of another time lag variable which will further delay the approach to steady state
How long to approach to 2 decimal places?
P1: 72 sec
τ1(2): 73.5 sec
τ2(4): 77 sec
τ(6): 80 sec

## Slide 19
Notes: All required modification to handle the additional equation in part 2

## Slide 20
Notes: Added additional Function

## Slide 21
Function func(t, Temp)
Double Precision, intent (in):: t, Temp
Double Precision:: func, M, F1, F2, T1, T2
M = 100.00
T1 = 25.00
T2 = 75.00
F2 = 5.00
!F1 is a function of time F1(t=0) = 5kg/s
If (t>=10.0) then
F1 = 4.00
else
F1 = 5.00 - 0.10*t
End if
!Sets the value of the function
func = 1/M*(F1*T1 + F2*T2 - (F1+F2)*Temp)
End Function
Function

## Slide 22
Notes: Added additional Function

## Slide 23: Integration Method
!Calculates the steps size and sets the initial values based on the input data
stepSize = (finalX - startX)/numSteps
xint(0) = startX
yint(0) = startY
!Do loop runs the interative calculation of the Integration Method
Do i = 0, numSteps - 1
yint(i+1) = yint(i) + stepSize*func(xint(i), yint(i))
xint(i+1) = xint(i) + stepSize
End Do
!The write_xy_data subroutine writes the data in the arrays to the specified data file
Call write_xy_data('/Users/DanielK/Desktop/Fortran/IntMethod.dat', numSteps, xint, yint, err)
!The run_gnuplot subroutine uses the given script to create a graph of the data
Call run_gnuplot('/Users/DanielK/Desktop/Fortran/IntMethod.txt')

## Slide 24
Notes: Only had to troubleshoot the RK Method for part 2 as the coefficients k1, k2, k3, k4 were not correct for when there are two variables to solve for

## Slide 25: Runge-Kutta Method
!Do loop runs the interative calculation of the RK Method
Do i = 0, numSteps - 1
k1 = stepSize*func(xrk(i), yrk(i))
k2 = stepSize*func((xrk(i)+stepSize/2), (yrk(i)+k1/2))
k3 = stepSize*func((xrk(i)+stepSize/2), (yrk(i)+k2/2))
k4 = stepSize*func((xrk(i)+stepSize), (yrk(i)+k3))
yrk(i+1) = yrk(i) + (k1 + 2.00*k2 + 2.00*k3 + k4)/6.00
xrk(i+1) = xrk(i) + stepSize
End Do
!The write_xy_data subroutine writes the data in the arrays to the specified data file
Call write_xy_data('/Users/DanielK/Desktop/Fortran/RKMethod.dat', numSteps, xrk, yrk, err)
!The run_gnuplot subroutine uses the given script to create a graph of the data
Call run_gnuplot('/Users/DanielK/Desktop/Fortran/RKMethod.txt')

## Slide 26
Notes: Adapted to handle additional variables to write into specific datafiles for different values of tau

## Slide 27: Combine Data
!Do loops inputs all the data from both solutions into a single array
Do i = 0, numSteps
allpts(i,0) = xint(i)
allpts(i,1) = yint(i)
allpts(i,2) = yrk(i)
End Do
!The run_gnuplot subroutine uses the given script to create a graph of the data
Call run_gnuplot('/Users/DanielK/Desktop/Fortran/IntRKMethod.txt')

## Slide 28
Notes: Adapted to handle additional variables to write into specific datafiles for different values of tau

## Slide 29: Write XY Data
open ( unit = file_unit, file = data_filename, status = 'replace', &
iostat = ios )
!Edited to start at i=0
do i = 0, n
write ( file_unit, * ) x(i), y(i)
end do
close ( unit = file_unit )
write ( *, '(a)' ) ' Wrote the GNUPLOT XY data file "' // &
trim ( data_filename ) // '"'

## Slide 30
Notes: Adapted to handle additional variables to write into specific datafiles for different values of tau

## Slide 31: Run GNUPlot
write ( command, * ) 'gnuplot ' // command_filename
write ( *, '(a)' ) ' '
write ( *, '(a)' ) 'GNUFOR:'
write ( *, '(a)' ) ' Issuing the command:"' // trim ( command ) // '".'

## Slide 32: Program Troubleshooting
This section outlines the procedure by which the program was tested to find the source of the error originally experienced.

## Slide 33
Error: T -> -Infinity
as t -> infinity
Notes: Error: T-> -Infinity as t-> infinity
Changed the way F1 was calculated, required if statement to determine if it was past t=10s

## Slide 34: Change
!F1 is a function of time F1(t=0) = 5kg/s
If (t>=10.0) then
F1 = 4.00
else
F1 = 5.00 - 0.10*t
End if
F1 = 5.00 - 0.10*t

## Slide 35
Error: T(t=0) = 0 on graph
Notes: Error: Starting value = 0 on graph
This subroutine came from: http://people.sc.fsu.edu/~jburkardt/f_src/gnufor/gnufor.html and required modifying the input array such that the index started form 0

## Slide 36: Change
real ( kind = 8 ) x(0:n)
real ( kind = 8 ) y(0:n)
real ( kind = 8 ) x(n)
real ( kind = 8 ) y(n)

## Slide 37: Part 1 Graph

## Slide 38: Program Modification for Part 2
This section outlines the procedure by which the program was adapted to solve part 2 of the problem.

## Slide 39
Notes: Added additional Function

## Slide 40: Additional Function
Function func(t, F1, tau)
Double Precision, intent (in):: t, F1
Double Precision:: func, F1spec, tau
!tau = 2.00
!F1spec is a function of time F1(t=0) = 5kg/s
F1spec = 5.00 - 0.10*t
!Sets the value of the function
func = 1/tau*(F1spec - F1)
End Function

## Slide 41
Notes: Added additional Function

## Slide 42: Integration Method Modification
!Do loop runs the interative calculation of the Integration Method
Do i = 0, numSteps - 1
xint(i+1) = xint(i) + stepSize
yint(i+1) = yint(i) + stepSize*func(xint(i), yint(i), tauin)
zint(i+1) = zint(i) + stepSize*func2(xint(i), yint(i), zint(i))
End Do

## Slide 43
Notes: Only had to troubleshoot the RK Method for part 2 as the coefficients k1, k2, k3, k4 were not correct for when there are two variables to solve for

## Slide 44: Runge-Kutta Modification
!Do loop runs the interative calculation of the RK Method
Do i = 0, numSteps - 1
xrk(i+1) = xrk(i) + stepSize
k1 = stepSize*func(xrk(i), yrk(i), tauin)
k2 = stepSize*func((xrk(i)+stepSize/2), (yrk(i)+k1/2), tauin)
k3 = stepSize*func((xrk(i)+stepSize/2), (yrk(i)+k2/2), tauin)
k4 = stepSize*func((xrk(i)+stepSize), (yrk(i)+k3), tauin)
yrk(i+1) = yrk(i) + (k1 + 2.00*k2 + 2.00*k3 + k4)/6.00
k1z = stepSize*func2(xrk(i), yrk(i), zrk(i))
k2z = stepSize*func2((xrk(i)+stepSize/2), (yrk(i)+k1/2), (zrk(i)+k1z/2))
k3z = stepSize*func2((xrk(i)+stepSize/2), (yrk(i)+k2/2), (zrk(i)+k2z/2))
k4z = stepSize*func2((xrk(i)+stepSize), (yrk(i)+k3), (zrk(i)+k3z))
zrk(i+1) = zrk(i) + (k1z + 2.00*k2z + 2.00*k3z + k4z)/6.00
End Do

## Slide 45
Notes: Adapted to handle additional variables to write into specific datafiles for different values of tau

## Slide 46: Combined Data Modification
!The run_gnuplot subroutine uses the given script to create a graph of the data
Call run_gnuplot('/Users/DanielK/Desktop/Fortran/IntRKMethod_'//namein//'.txt')

## Slide 47: Part 2 Graphs